## Slide 1: Computer Networks
张 辉
hzhang@buaa.edu.cn
82338088
Textbook
  计算机网络（第七版） 谢希仁 电子工业出版社
  Computer Networking: A Top-Down Approach Featuring the Internet by Kurose and Ross （高等教育出版社）
  Computer Networks by A. Tanenbaum

## Slide 2: 教学内容
计算机网络是计算机技术与通信技术的交叉学科。
本课程以计算机网络体系结构为总纲，系统、分层次地讲述计算机网络的基本概念和工作原理，包括物理层、数据链路层、网络层、传输层和应用层的功能和主要协议，重点介绍Internet核心协议族TCP/IP。

## Slide 3: 教学目标
了解有关计算机网络的基本概念，掌握计算机网络的基本工作原理和主要技术，理解计算机网络应用原理及其方法。
以计算机网络体系结构的分层模型为基础，重点掌握Internet。深入了解TCP/IP协议族的工作原理，为今后各种计算机网络及其相关应用、学习和研究打下基础。

## Slide 4: 关于成绩
期末考试 90%
  上课主要内容
平时作业 5%
  教材习题
大作业 5%
  网络程序

## Slide 5: What Will We Cover?
网络简介
网络体系结构
网络物理层（传输媒介、接口、信号、性能指标）
数据链路层（网络检错、同步、HDLC、PPP、广域网）
局域网技术（Ethernet、Token Ring、Token bus 等)
网络层（IP 编址、subnetting、VLSM、CIDR 、 IPv6 ）
路由原理（RIP、OSPF、BGP）
传输层（TCP 、UDP）
应用层（SMTP、ftp、Web、DNS等）
网络安全及网络管理 （非重点）
网络新技术(Mobile、Multicasting、Overlay等)（非重点）

## Slide 6: 计算机网络在信息时代的作用
21 世纪的一些重要特征就是数字化、信息化和网络化，它是一个以互联网为核心的信息时代。当前:智能化、知识化
网络现已成为信息社会的命脉和发展知识经济的重要基础。
网络常见的“三网”，即电信网络（3G/4G/5G）、有线电视网络（Cable Modem）和计算机网络（校园网等）。
发展最快的并起到核心作用的是计算机网络（Internet）。

## Slide 7: 网络之间关系及三网融合（IP）

## Slide 8: 计算机网络发展的四个阶段
计算机通讯技术发展
  面向终端的数据通讯（50年代初，SAGE）
计算机网络的形成
  分组交换网的出现（1969年ARPANET）
网络体系结构的研究及应用
  Decnet、SNA、ISO/OSI、TCP/IP（1983正式成为ARPANET协议）
互联网的出现与应用
  Internet、无线网、物联网
  大数据、云计算

## Slide 9: 第一阶段代表：SAGE
20世纪50年代建立于美国的半自动地面防空系统SAGE:把远距离的雷达通过通信线路送到一台旋风型计算机上进行处理和控制，首次实现了计算机和通信的结合。特点:
（1）以主机为中心，终端没有独立数据处理能力。（2）主机通过串行接口RS-232与多用户系统相连接，同时承担数据处理和通信任务，主机负担较重。 （3）终端运行速度慢，每个用户独占一条通信线路，线路利用率较低。（4）这种结构属于集中控制方式，可靠性低。

## Slide 10
实现了分布式的资源共享。
具有分组交换的数据交换方式。
采用专门的通信控制处理机。
资源子网：由主机、终端、终端控制器、联网外设、各种软件资源与信息资源组成，它负责全网的数据处理并向网络用户提供各种网络资源与服务。
通信子网:由通信控制处理机、通信线路和其他通信设备组成，负责网络数据传输、转发等通信处理任务。
第二代计算机网络（分组交换）

## Slide 11: 计算机网络的构成
计算机网络运行在通信传输子网之上，由用户资源子网和通信
传输子网组成业务网。互联网叫Core 和 Edge。
主要功能：连通性和共享

## Slide 12
通信传输子网（network core）
Communication networks
Broadcast networks
End nodes share a common channel (TV, radio…)
Switched networks
end nodes send to one (or more) end nodes
Packet switching
Data sent in discrete portions
(the Internet)
Circuit switching
Dedicated circuit per call
(telephone, ISDN)
(physical)
Datagram networks
Each packet switched independently
Virtual circuit networks
Pre-established path
(logical)

## Slide 13: 电路交换: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required
resource piece idle if not used by owning call (no sharing)
交换：多个节点之间通过线路进行转接，实现信号的联通

## Slide 14: Circuit Switching
A node (switch) in a circuit switching network
incoming links
outgoing links
Node

## Slide 15: Circuit Switching Steps
Three phases
  circuit establishment
  data transfer
  circuit termination
If circuit not available: “Busy signal”
Examples
  Telephone networks
  ISDN (Integrated Services Digital Networks)

## Slide 16: Circuit Switching: FDM and TDM
FDM：Frequency-division multiplexing
frequency
time
TDM：
frequency
time
4 users
Example:
Time Division Multiplexing
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 17: Circuit Switching Telephone Network
Source
“Caller”
Central
Office
“C.O.”
Destination
“Callee”
Central
Office
“C.O.”
Trunk
Exchange
Each phone call is allocated 64kb/s. So, a 2.5Gb/s trunk line can carry about 39,000 calls.

## Slide 18
分组 packet
邮政系统
  信件－收信人地址－发信人地址
数据报(DataGram)
  自带寻址信息
  能独立地从数据源“行走”到目的终点的数据包(packet)
分组交换：通信双方以分组为单位、使用存储-转发机制实现数据交互的通信方式

## Slide 19: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed,
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  transmit over link
  wait turn at next link
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 20: Network Core: Packet Switching
Packet-switching versus circuit switching: human restaurant analogy
other human analogies?
A
B
C
10 Mbs
Ethernet
1.5 Mbs
45 Mbs
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 21: Packet Switching – Statistical Multiplexing
Switches arbitrate between inputs
Can send from any input that’s ready
  Links never idle when traffic to send
  (Efficiency!)
Packets
21

## Slide 22
Data are sent as formatted bit-sequences, so-called packets.
Packets have the following structure:
    Header and Trailer carry control information (e.g., destination address, check sum)
Each packet is passed through the network from node to node along some path (Routing)
At each node the entire packet is received, stored briefly, and then forwarded to the next node (Store-and-Forward Networks)
Header
Data
Trailer
Packet Structure and switching

## Slide 23: Packet Switching
A node in a packet switching network
incoming links
outgoing links
Node
Memory

## Slide 24: Packet Switching：Routing
A
R1
R2
R4
R3
B
Source
Destination
It’s the method used by the Internet.
Each packet is individually routed packet-by-packet, using the router’s local routing table.
The routers maintain no per-flow state.
Different packets may take different paths.
Several packets may arrive for the same output link at the same time, therefore a packet switch has buffers.

## Slide 25: Packet-switched networks: routing
Goal: move packets among routers from source to destination
  we’ll study several path selection algorithms
datagram network:
  destination address determines next hop
  routes may change during session
  analogy: driving, asking directions
virtual circuit network:
  each packet carries tag (virtual circuit ID), tag determines next hop
  fixed path determined at call setup time, remains fixed thru call
  routers maintain per-call state

## Slide 26
Virtual circuit network
A
B
C
D
E
1
2
3
3
2
1
1
3
2
1
2
3
1
1
2
2
3
3
2
3
1
SVC 1
SVC 2
Note: Packet headers don’t need to contain the full destination
address of the packet - only contain virtual circuit identifier (VCI)

## Slide 27: 分组交换vs. 电路交换
1 Mb/s链路
每个用户:
  100Kb/s 当“激活”
  激活时间为 10%
电路交换:
  10 用户
分组交换:
  对 35个用户来说, 概率: > 10个用户同时激活小于 .0004
分组交换使得更多用户可“同时”使用网络!
N users
1 Mbps link

## Slide 28: 三种交换的比较
P1
P2
P3
P4
P1
P2
P3
P4
P3
P4
报
文
报
文
报
文
A B C D
A B C D
A B C D
报文交换
电路交换
分组交换
t
连接建立
数据传送
报文
P2
P1
连接释放
数据传送
的特点
比特流直达终点
报文
报文
报文
分组
分组
分组
存储
转发
存储
转发
存储
转发
存储
转发

## Slide 29: Delay in packet-switched networks
packets experience delay on end-to-end path
four sources of delay at each hop
nodal processing:
  check bit errors
  determine output link
queueing
  time waiting at output link for transmission
  depends on congestion level of router
A
B
propagation
transmission
nodal
processing
queueing

## Slide 30: Delay in packet-switched networks
Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 31: 四种时延所产生的地方
1 0 1 1 0 0 1
…
发送器
队列
在链路上产生
传播时延
结点 B
结点 A
在发送器产生传输时延
(即发送时延)
在结点 A 中产生
处理时延和排队时延
数据
从结点 A 向结点 B 发送数据
链路

## Slide 32: Queueing delay
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1
Little's Law ：一个排队系统在稳定状态下，在系统里面的个体数量平均值 L，等于平均个体到达率λ （单位是个每单位时间）乘以个体的平均逗留时间W。

## Slide 33: 时延(delay 或 latency)
传输时延（发送时延 ） 发送数据时，数据块从结点进入到传输媒体所需要的时间。 Transmission delay
也就是从发送数据帧的第一个比特算起，到该帧的最后一个比特发送完毕所需的时间。
发送时延 =
数据块长度（比特）
信道带宽（比特/秒）

## Slide 34: 时延(delay 或 latency)
传播时延 电磁波在信道中需要传播一定的距离而花费的时间。 Propagation delay
信号传输速率（即发送速率）和信号在信道上的传播速率是完全不同的概念。
传播时延 =
信道长度（米）
信号在信道上的传播速率（米/秒）

## Slide 35: Packet Switching Delay
Host A
Host B
R1
R2
R3
A
R1
R2
R4
R3
B
TRANSP1
TRANSP2
TRANSP3
TRANSP4
PROP1
PROP2
PROP3
PROP4
Source
Destination
“Store-and-Forward” at each Router

## Slide 36: Packet vs Message Switching Why not send the entire message in one packet?
总报文长度为M，传输速率为R，每一段传播延时为PROP，每小段长度为m，中间经过n个交换设备
Breaking message into packets allows parallel transmission across all links, reducing end to end latency. It also prevents a link from being “hogged” for a long time by one message.
Host A
Host B
R1
R2
R3
M/R
Host A
Host B
R1
R2
R3
M/R

## Slide 37: 计算机网络的性能指标
1. 速率
比特（bit）是计算机中数据量的单位，也是信息论中使用的信息量的单位。
Bit 来源于 binary digit，意思是一个“二进制数字”，因此一个比特就是二进制数字中的一个 1 或 0。
速率即数据率(data rate)或比特率(bit rate)是计算机网络中最重要的一个性能指标。速率的单位是 b/s，或kb/s, Mb/s, Gb/s 等
速率往往是指额定速率或标称速率。
2.带宽
“带宽”(bandwidth)本来是指信号具有的频带宽度，单位是赫（或千赫、兆赫、吉赫等）。
现在“带宽”是数字信道所能传送的“最高数据率”的同义语，单位是“比特每秒”，或 b/s (bit/s)。

## Slide 38: 常用的带宽单位
更常用的带宽单位是
  千比每秒，即 kb/s （103 b/s）
  兆比每秒，即 Mb/s（106 b/s）
  吉比每秒，即 Gb/s（109 b/s）
  太比每秒，即 Tb/s（1012 b/s）
请注意：在计算机界，K = 210 = 1024
M = 220, G = 230, T = 240。
1Mbyte = 1024Kbyte

## Slide 39: Symbols （注意区别）
Mbps
  megabits per second 106 bits per second
MBps
  megabytes per second
Gbps, Kbps,
bandwidth
  the total information flow over a given time

## Slide 40: 数字信号流随时间的变化
在时间轴上信号的宽度随带宽的增大而变窄。
每秒 106 个比特
时间
1 0 1 0 1 1
1 s
带宽为
1 Mb/s
时间
每秒 4  106 个比特
0.25 s
带宽为
4 Mb/s

## Slide 41: 吞吐量
吞吐量(throughput)表示在单位时间内通过某个网络（或信道、接口）的数据量。
吞吐量用于对现实世界中的网络的一种测量，以便知道实际上到底有多少数据量能够通过网络。throughput: rate (bits/time unit) at which bits transferred between sender/receiver
吞吐量受网络的带宽或网络的额定速率的限制。
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 42: 时延带宽积
（传播）时延
链路
带宽
时延带宽积 = 传播时延  带宽
链路的时延带宽积又称为以比特为单位的链路长度。
时延带宽积

## Slide 43: 利用率
信道利用率指出某信道有百分之几的时间是被利用的（有数据通过）。完全空闲的信道的利用率是零。
网络利用率则是全网络的信道利用率的加权平均值。
信道利用率并非越高越好。

## Slide 44: 时延与网络利用率的关系
根据排队论的理论，当某信道的利用率增大时，该信道引起的时延也就迅速增加。
若令 D0 表示网络空闲时的时延，D 表示网络当前的时延，则在适当的假定条件下，可以用下面的简单公式表示 D 和 D0之间的关系：
U 是网络的利用率，数值在 0 到 1 之间。

## Slide 45
时延 D
利用率 U
1
0
D0
时延
急剧
增大

## Slide 46: Numerical example
How long does it take to send a file of 80K bytes from host A to host B by using one link over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots
  500 msec to establish end-to-end circuit
Work it out!
Rate 1.536 Mbps /24 = 64,000 bps
Total time 500ms+ 80K*8b/64kbps=10500 ms

## Slide 47: 分组交换vs. 电路交换
在突发性数据传输过程中表现优异
  资源共享
  无须事先建立连接
过度拥塞: 导致分组延迟和丢失
  需要协议来保障可靠的数据传输, 拥塞控制
Q: 如何在分组交换网中提供电路交换的性能?
  为音频/视频（audio/video）应用提供带宽保障
  仍然是一个需要解决的问题
分组交换是不是 “winner”?

## Slide 48: Why does the Internet use packet switching?
Efficient use of expensive links:
  The links are assumed to be expensive and scarce.
  Packet switching allows many, bursty flows to share the same link efficiently.
  “Circuit switching is rarely used for data networks, ... because of very inefficient use of the links” - Gallager
Resilience to failure of links & routers:
  ”For high reliability, ... [the Internet] was to be a datagram subnet, so if some lines and [routers] were destroyed, messages could be ... rerouted” - Tanenbaum
Source: Networking 101
Notes: Breaking message into packets allows parallel transmission across all links, reducing network latency.
In summary the benefits that of packet switched networks can be summarized as follows:
They use the bandwidth efficiently, meaning that a trunk link uses less resources than the sum of its tributaries, as they multiplex and conserve bandwidth
They have little state in the intermediate nodes
They are robust, some claim that they were designed to withstand a nuclear attack
They do not have a central authority from whom we need permission to run experiments

## Slide 49
第三代:网络体系结构
网络体系结构：计算机之间相互通信的层次以及各层中的协议和层次之间接口的集合
ISO/OSI 与 TCP/IP
  What is layering?
  Why layering?
  ISO/OSI layering and Internet layering
  How to determine the layers: the end-to-end arguments

## Slide 50: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?
Or at least our discussion of networks?

## Slide 51: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 52: Organization of air travel: a different view
Layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 53: Layered air travel: services
Counter-to-counter delivery of person+bags
baggage-claim-to-baggage-claim delivery
people transfer: loading gate to arrival gate
runway-to-runway delivery of plane
airplane routing from source to destination

## Slide 54: Distributed implementation of layer functionality
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Departing airport
arriving airport
intermediate air traffic sites
airplane routing
airplane routing

## Slide 55: 会话分层模型

## Slide 56: 分层模型带来的好处
1、容易解决通信的异质性（heterogeneity）问题
语言层解决不同种语言的相互翻译：（汉-英）
媒介层解决信息传递：语音（电话）/文字（传真）
2、使复杂问题简化，高层屏蔽低层细节问题
概念层只关心会话内容，不关心语种和会话方式
语言层只关心语种，不关心会话内容和方式
媒介层只关心信息的传递，不关心信息的内容
3、使设计容易实现
每个层次向上一层提供服务
每个层次向下一层请求服务

## Slide 57: 会话分层模型对应的协议族
•协议族
每一层次定义确定的规则
这些分层的规则构成协议族
用协议族实现通信过程
•“两人会话”的协议族
媒介层：双方不能同时讲话
语言层：双方使用同种语言
概念层：双方对话题具有共同知识背景

## Slide 58: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg transmission, receipt

## Slide 59: What’s a protocol?
a human protocol and a computer network protocol:
Q: Other human protocol?
Hi
Hi
Got the
time?
2:00
TCP connection
req.
TCP connection
reply.
Get http://www.buaa..edu.cn/index.htm
<file>
time

## Slide 60: 协议 protocol
协议：计算机网络同等层次中，通信双方进行信息交换时必须遵守的规则。
  协议的组成：
  1. 语法（syntax)：表示数据与控制信息的结构或格式
  语义（semantics)：指出需要发出何种控制信息、完成何种动作以及做出何种响应
  定时（timing)：有关事件顺序的说明
  或者叫同步

## Slide 61: 分层优点
    各层独立。每一层不需要知道下层是如何实现的，只需要知道层间的接口和所提供的服务。
    灵活性好。当任意层发生变化时，只要接口不变，上下层均不受影响。
    结构上分开，各层可采用最适合的技术。
    易于实现和维护。
    促进标准化。由于每一层及其提供的服务都有明确的定义。

## Slide 62: An Example: No Layering
No layering: each new application has to be re-implemented for every network technology!
Telnet
FTP
packet
radio
coaxial
cable
fiber
optic
Application
Transmission
Media
HTTP

## Slide 63: An Example: Benefit of Layering
Solution: introduce an intermediate layer that provides a common abstraction for various network technologies
HTTP
Telnet
FTP
packet
radio
coaxial
cable
fiber
optic
Application
Transmission
Media
Transport
& Network

## Slide 64: 计算机网络体系结构
1、定义
层次结构和协议的集合构成网络的体系结构。
2、作用
复杂网络的抽象概念描述，形成网络的框架结构，实现网络的结构化设计；
对每一层进行功能界定，成为该层次的实现者进行软件编程和硬件设计的依据。
3 、研究方法
按功能抽象分层
定义层间的结构和提供的服务
定义同层间通信的规则—协议

## Slide 65: 分层原则
    根据功能需要分层
    每层的功能明确
    每层的功能选择有利于指定国际标准
    每层的接口信息量尽可能少
    层数足够多：避免不同的功能混于同一层
    6. 层数不能太多：避免体系结构过于庞大

## Slide 66: ISO OSI Reference Model
Seven layers
  lower three layers are hop-by-hop
  next four layers are end-to-end
Application
Presentation
Session
Transport
Network
Datalink
Physical
Application
Presentation
Session
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Physical medium
segment
packet
Frame
bit
message
message
message

## Slide 67: 主机 1 向主机 2 发送数据
5
4
3
2
1
5
4
3
2
1
主机 1
AP2
AP1
主机 2
应 用 程 序 数 据
应用层首部
H5
10100110100101 比 特 流 110101110101
注意观察加入或剥去首部（尾部）的层次
应 用 程 序 数 据
H5
应 用 程 序 数 据
H4
H5
应 用 程 序 数 据
H3
H4
H5
应 用 程 序 数 据
H4
运输层首部
H3
网络层首部
H2
链路层
首部
T2
链路层
尾部

## Slide 68: 网络体系结构的主要概念
1、每个层次定义三个基本概念
接口、服务和协议（协议是控制两个对等实体进行通信的规则的集合，协议能否100%正确和可靠？）
2、三个概念之间的相互关系
接口与服务的关系
协议与服务的关系（理解：协议是水平的、服务是垂直的）

## Slide 69: 每个层次定义的三个概念
1、接口
每层接口告诉上层进程对其的访问方式
定义需要的参数和预期的结果
2、服务
每层为上层提供服务，定义该层做什么
服务通常由一组原语操作来描述
3、协议
定义服务是如何实现的
每层中使用的对等协议只涉及该层的内部事物
协议的修改和替换不影响更高层次

## Slide 70: 协议复杂性
协议必须把所有不利的条件事先都估计到，而不能假定一切都是正常的和非常理想的。
看一个计算机网络协议是否正确，不能光看在正常情况下是否正确，而且还必须非常仔细地检查这个协议能否应付各种异常情况。

## Slide 71: 著名的协议举例 【例1-1】
占据东、西两个山顶的蓝军1和蓝军2与驻扎在山谷的白军作战。其力量对比是：单独的蓝军1或蓝军2打不过白军，但蓝军1和蓝军2协同作战则可战胜白军。现蓝军1拟于次日正午向白军发起攻击。于是用计算机发送电文给蓝军2。但通信线路很不好，电文出错或丢失的可能性较大（没有电话可使用）。因此要求收到电文的友军必须送回一个确认电文。但此确认电文也可能出错或丢失。试问能否设计出一种协议使得蓝军1和蓝军2能够实现协同作战因而一定（即100 %而不是99.999…%）取得胜利？

## Slide 72
明日正午进攻，如何？
同意
收到“同意”
收到：收到“同意”
…
…
…
…
…
…
这样的协议无法实现！

## Slide 73: 结 论
这样无限循环下去，两边的蓝军都始终无法确定自己最后发出的电文对方是否已经收到。
没有一种协议能够蓝军能 100% 获胜。

## Slide 74: Physical Layer (1)
Service: moves information between two systems connected by a physical link
透明传输比特流
Interface: specifies how to send a bit
Protocol: coding scheme used to represent a bit, voltage levels, duration of a bit
Examples: coaxial cable, optical fiber links; transmitters, receivers

## Slide 75: Datalink Layer (2)
Service:
  framing, i.e., attach frames separator
  send data frames between peers
  相邻结点间的链路上“透明” 传输帧
  others:
    arbitrates the access to common physical media
    ensures reliable transmission
    provides flow control
Interface: sends a data unit (frame) to a machine connected to the same physical media
Protocol: layer addresses, implement Medium Access Control (MAC) (e.g., CSMA/CD)…

## Slide 76: Network Layer (3)
Service:
  delivers a packet to a specified destination
  路由选择
  performs fragmentation/reassembly of packets
  others:
    packet scheduling (store&forward)
    buffer management
Interface: sends a packet to a specified destination
Protocol: defines global unique addresses; constructs routing tables; implement packet forwarding; fragments/reassembles packets

## Slide 77: Transport Layer (4)
Service:
  为两个主机进程间的通讯提供服务
  provides an in-order, error-free, and flow and congestion controlled end-to-end connection
  multiplex/demuliplex packets
Interface: sends a packet to a destination
Protocol: implements reliability, as well as flow and congestion control
Examples: TCP and UDP
  TCP: in-order, error free, flow and congestion control

## Slide 78: Session Layer (5)
Service:
  full-duplex/half full-duplex
  access management, e.g., token control
  synchronization, e.g., provide check points for long transfers
Interface: depends on service
Protocols: token management; insert checkpoints, implement roll-back functions

## Slide 79: Presentation Layer (6)
Service: converts data between various representations
数据压缩/解压、加密、解密
Interface: depends on service
Protocol: defines data formats and rules to convert from one format to another

## Slide 80: Application Layer (7)
Service: any service provided to end users
为用户的应用进程提供服务
Interface: depends on the application
Protocol: depends on the application
Examples: FTP, Telnet, WWW

## Slide 81: 对OSI的评价
OSI是80年代计算机网络技术，网络体系结构的主流
OSI网络体系结构的贡献：
  分层模型
  服务、接口、协议
Andrew S. Tanenbaum 在书中评价OSI：
  糟糕的提出时机（太晚，周期太长）
  糟糕的技术（模型和协议都有缺陷，不合理）
  糟糕的实现（庞大，笨拙，缓慢，复杂）
  糟糕的策略（政府和组织的官僚，效率低）

## Slide 82: 第四代网络：Internet
goal:
overview, “feel” of networking
more depth, detail later in course
approach:
  descriptive
  use Internet as example
Overview:
what’s the Internet
what’s a protocol?
network edge
network core
access net, physical media
performance: loss, delay
protocol layers, service models
backbones, NAPs, ISPs
Network history

## Slide 83: What’s the Internet: “nuts and bolts” view
Introduction
1-83
millions of connected computing devices: hosts = end systems
  running network apps
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
  transmission rate = bandwidth
routers: forward packets (chunks of data)
Notes: 83

## Slide 84: What’s the Internet: “nuts and bolts” view
Introduction
1-84
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, Ethernet
Internet: “network of networks”
  loosely hierarchical
  public Internet versus private intranet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
Notes: 84

## Slide 85: What’s the Internet: a service view
Introduction
1-85
communication infrastructure enables distributed applications:
  Web, VoIP, email, games, e-commerce, file sharing
communication services provided to apps:
  reliable data delivery from source to destination
  “best effort” (unreliable) data delivery
Notes: 85

## Slide 86: Who is Who on the Internet ?
Internet Architecture Board (IAB): The IAB is responsible for defining the overall architecture of the Internet, providing guidance and broad direction to the IETF.
Internet Engineering Task Force (IETF): The IETF is the protocol engineering and development arm of the Internet. Subdivided into many working groups, which specify Request For Comments or RFCs.
IRTF (Internet Research Task Force): The Internet Research Task Force is a composed of a number of focused, long-term and small Research Groups.
The Internet Engineering Steering Group (IESG): The IESG is responsible for technical management of IETF activities and the Internet standards process. Standards. Composed of the Area Directors of the IETF working groups.

## Slide 87: 关于因特网的标准化工作
因特网协会 ISOC
因特网研究指导小组
IRSG
因特网研究部 IRTF
因特网工程部 IETF
因特网工程指导小组
IESG
…
RG
WG
…
…
RG
…
领域
领域
因特网体系结构
研究委员会 IAB
WG
WG
WG

## Slide 88: Internet Standardization Process
All standards of the Internet are published as RFC (Request for Comments). But not all RFCs are Internet Standards !
  available: http://www.ietf.org
A typical (but not only) way of standardization is:
  Internet Drafts
  Proposed Standard
  Draft Standard (requires 2 working implementation)
  Internet Standard (declared by IAB)
David Clark, MIT, 1992: "We reject: kings, presidents, and voting. We believe in: rough consensus and running code.”

## Slide 89: 各种RFC之间的关系
因特网草案
建议标准
草案标准
因特网标准
历史的 RFC
实验的 RFC
提供信息的 RFC
6 种 RFC

## Slide 90: A closer look at network structure:
Introduction
1-90
network edge: applications and hosts
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
Notes: 90

## Slide 91: The network edge:
Introduction
1-91
end systems (hosts):
  run application programs
  e.g. Web, email
  at “edge of network”
client/server
peer-peer
client/server model
  client host requests, receives service from always-on server
  e.g. Web browser/server; email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
  e.g. Napster, Gnutella, BitTorrent
Notes: 91

## Slide 92: 客户端和服务器端的特点
客户端
  被用户调用后运行，在打算通信时主动向远地服务器发起通信（请求服务）。因此，客户程序必须知道服务器程序的地址。
  不需要特殊的硬件和很复杂的操作系统。
服务器端
  一种专门用来提供某种服务的程序，可同时处理多个远地或本地客户的请求。
  系统启动后即自动调用并一直不断地运行着，被动地等待并接受来自各地的客户的通信请求。因此，服务器程序不需要知道客户程序的地址。
  一般需要强大的硬件和高级的操作系统支持。

## Slide 93
运行
客户
程序
网络边缘
网络核心
运行
服务器
程序
A
B
① 请求服务
② 得到服务
客户
服务器
客户/服务器模式

## Slide 94: Network edge: connection-oriented service
Goal: data transfer between end sys.
handshaking: setup (prepare for) data transfer ahead of time
  Hello, hello back human protocol
  set up “state” in two communicating hosts
TCP - Transmission Control Protocol
  Internet’s connection-oriented service
TCP service [RFC 793]
reliable, in-order byte-stream data transfer
  loss: acknowledgements and retransmissions
flow control:
  sender won’t overwhelm receiver
congestion control:
  senders “slow down sending rate” when network congested

## Slide 95: Network edge: connectionless service
Goal: data transfer between end systems
  same as before!
UDP - User Datagram Protocol [RFC 768]: Internet’s connectionless service
  unreliable data transfer
  no flow control
  no congestion control
App’s using TCP:
HTTP (WWW), FTP (file transfer), Telnet (remote login), SMTP (email)
App’s using UDP:
streaming media, teleconferencing, Internet telephony

## Slide 96: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 97: Access networks
Introduction
1-97
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?
Notes: 97

## Slide 98: Access net: digital subscriber line (DSL)
central office
ISP
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  use existing telephone line to central office DSLAM(Access Multiplexer:接入复用器)
    data over DSL phone line goes to Internet
    voice over DSL phone line goes to telephone net
  < 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
  < 24 Mbps downstream transmission rate (typically < 10 Mbps)
DSL
modem
splitter
DSL access
multiplexer

## Slide 99
Access net: cable network
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
frequency division multiplexing: different channels transmitted
in different frequency bands

## Slide 100: FTTP Architecture (Fiber to the Premises )
100
Optical Network Terminal (ONT) box outside dwelling or business
Fiber Distribution Terminal (FDT) in poles or pedestals
Fiber Distribution Hub (FDH) at street cabinet
Optical Line Terminal (OLT) at central office

## Slide 101: Institutional access: local area networks
company/univ local area network (LAN) connects end system to edge router
Ethernet:
  shared or dedicated cable connects end system and router
  10 Mbs, 100Mbps, Gigabit Ethernet
deployment: institutions, home LANs soon

## Slide 102: Wireless access networks
shared wireless access network connects end system to router
wireless LANs:
  radio spectrum replaces wire
  e.g., Lucent Wavelan 10 Mbps
wider-area wireless access
  CDPD: wireless access to ISP router via cellular network
base
station
mobile
hosts
router

## Slide 103: Home network components
ADSL or cable modem
router/firewall/NAT (Network Address Translation)
  NAT enables a LAN to use one set of IP addresses for internal traffic and a second set of addresses for external traffic. It makes all necessary IP address translations.
Ethernet
wireless access point
wireless
access
point
wireless
laptops
router/
firewall
cable
modem
to/from
cable
headend
Ethernet

## Slide 104
Internet Layering and OSI Layering
OSI: conceptually define: service, interface, protocol
Internet: provide a successful implementation
Application
Presentation
Session
Transport
Network
Datalink
Physical
Internet
Host-to-
network
Transport
Application
IP
LAN
Packet
radio
TCP
UDP
Telnet
FTP
DNS

## Slide 105: 对TCP/IP的评价
TCP/IP是Internet的支撑协议，是目前使用最广泛的协议。
TCP/IP网络体系结构的主要优点：
  简单、灵活、易于实现
  充分考虑不同用户的需求
Andrew S. Tanenbaum 在书中评价TCP/IP：
  没有明显区分出协议、接口和服务的概念
  不通用，只能描述它本身
  不区分物理层和数据链路层
  有缺陷的协议很难被替换

## Slide 106: 连接类型的差别
网络层 传输层
面向连接 无连接 面向连接 无连接
ISO/OSI
TCP/IP IP TCP UDP

## Slide 107: Internet protocol stack
application: supporting network applications
  ftp, smtp, http
transport: host-host (进程间) data transfer
  tcp, udp
network: routing of datagrams from source to destination
  ip, routing protocols
link: data transfer between neighboring network elements
  ppp, ethernet
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 108: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Each layer:
distributed
“entities” implement layer functions at each node
entities perform actions, exchange messages with peers

## Slide 109: Layering: logical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
E.g.: transport
take data from app
add addressing, reliability check info to form “datagram”
send datagram to peer
wait for peer to ack receipt
analogy: post office
data
transport
transport
ack

## Slide 110: Layering: physical communication
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data

## Slide 111: Protocol layering and data
Each layer takes data from above
adds header information to create new data unit
passes new data unit to layer below
application
transport
network
link
physical
application
transport
network
link
physical
source
destination
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
M
M
M
M
H
t
H
t
H
n
H
t
H
n
H
l
message
segment
packet
frame

## Slide 112
The Hourglass Architecture of the Internet
IP
Ethernet
FDDI
Wireless
TCP
UDP
Telnet
Email
FTP
WWW

## Slide 113: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.

## Slide 114: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP

## Slide 115: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C

## Slide 116: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network

## Slide 117: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP

## Slide 118: Tier-1 ISP: e.g., Sprint
Introduction
1-118
…
to/from customers
peering
to/from backbone
….
…
…
…
POP: point-of-presence
Notes: 118

## Slide 119: Internet structure: network of networks
Introduction
1-119
“Tier-3” ISPs and local ISPs
  last hop (“access”) network (closest to end systems)
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Local and tier- 3 ISPs are customers of
higher tier ISPs
connecting them to rest of Internet
Notes: 119

## Slide 120: Internet structure: network of networks
Introduction
1-120
a packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP
Notes: 120

## Slide 121: Internet structure: network of networks
roughly hierarchical
national/international backbone providers (NBPs)
  e.g. BBN/GTE, Sprint, AT&T, IBM, UUNet
  interconnect (peer) with each other privately, or at public Network Access Point (NAPs)
regional ISPs
  connect into NBPs
local ISP, company
  connect into regional ISPs
NBP A
NBP B
NAP
NAP
regional ISP
regional ISP
local
ISP
local
ISP

## Slide 122: National Backbone Provider
e.g. BBN/GTE US backbone network

## Slide 123: Internet历史
1961: Kleinrock - queueing theory shows effectiveness of packet-switching
1964: Baran - packet-switching in military nets
1967: ARPAnet conceived by Advanced Reearch Projects Agency
1969: first ARPAnet node operational
1972:
  ARPAnet demonstrated publicly
  NCP (Network Control Protocol) first host-host protocol
  first e-mail program
  ARPAnet has 15 nodes
1961-1972: Early packet-switching principles

## Slide 124: A Brief History of the Internet
1969
  ARPANET commissioned: 4 nodes, 50kbps

## Slide 125: Initial Expansion of the ARPANET
Dec. 1969
March 1971
July 1970
Apr. 1972
Sep. 1972

## Slide 126
1970: ALOHAnet satellite network in Hawaii
1974: Cerf and Kahn - architecture for interconnecting networks
1976: Ethernet at Xerox PARC
late70’s: proprietary architectures: DECnet, SNA, XNA
late 70’s: switching fixed length packets (ATM precursor)
1979: ARPAnet has 200 nodes
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture
1972-1980: Internetworking, new and proprietary nets
Internet history

## Slide 127
1983: deployment of TCP/IP
1982: smtp e-mail protocol defined
1983: DNS defined for name-to-IP-address translation
1985: ftp protocol defined
1988: TCP congestion control
new national networks: Csnet, BITnet, NSFnet, Minitel
100,000 hosts connected to confederation of networks
1980-1990: new protocols, a proliferation of networks
Internet history

## Slide 128
early 1990’s: ARPAnet decommissioned
1991: NSF lifts restrictions on commercial use of NSFnet (decommissioned, 1995)
early 1990s: Web
  hypertext [Bush 1945, Nelson 1960’s]
  HTML, HTTP: Berners-Lee
  1994: Mosaic, later Netscape
  late 1990’s: commercialization of the Web
late 1990’s – 2000’s:
more killer apps: instant messaging, P2P file sharing
network security to forefront
est. 50 million host, 100 million+ users
backbone links running at Gbps
1990, 2000’s: commercialization, the Web, new apps
Internet history

## Slide 129
2005-present
~750 million hosts
  Smartphones and tablets
Aggressive deployment of broadband access
Increasing ubiquity of high-speed wireless access
Emergence of online social networks:
  Facebook: soon one billion users
Service providers (Google, Microsoft) create their own networks
  Bypass Internet, providing “instantaneous” access to search, emai, etc.
E-commerce, universities, enterprises running their services in “cloud” (eg, Amazon EC2)
Internet history

## Slide 130: NFSnet

## Slide 131
Internet Backbones in North America

## Slide 132
Notes: http://www.nthelp.com/images/BBNplanet.jpg

## Slide 134
Notes: http://www.nthelp.com/images/uunet.pdf

## Slide 136: http://moat.nlanr.net/Software/Cichlid/gallery/cheap_callouts.html

## Slide 137
Notes: http://moat.nlanr.net/Software/Cichlid/gallery/fakevbns-shot1.html
http://research.lumeta.com/ches/map/index.html

## Slide 138
Notes: http://research.lumeta.com/ches/map/gallery/isp-ss.gif
http://www.nthelp.com/maps.htm

## Slide 139
美国主干
欧洲主干
租用横穿大西洋的线路
租用至亚洲的的线路
地区网
国家网
隧 道
IP令牌总线局域网
IP令牌环局域网
IP以太局域网

## Slide 140
Global Terrabit Research Network (GTRN)

## Slide 142
南京
合肥
重庆
上海
福州
广州
昆明
郑州
北京
西安
武汉
长沙
南昌
南宁
湛江
海口
成都
长春
深圳
沈阳
地区中心 地区主节点 网管系统
桂林
2.5G 干 线
杭州
石家庄
太原
青岛
哈尔滨
济南
天津
大连
厦门
CERNET & CERNET2

## Slide 143
北 大
清 华
GSR12012
GSR12008
POS OC-48
GE
DPT Ring
北 航
GSR12008
北 邮
GSR12008
基 金委
GSR12008
中 科 院
GSR12008
CERNET
CSTNET
APAN/STARTAP
NSFCNET

## Slide 144: Internet Physical Infrastructure
144
Backbone ISP
ISP
ISP
Residential access
  Cable
  Fiber
  DSL
  Wireless
Campus access, e.g.,
  Ethernet
  Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)

## Slide 145: Internet Logical Infrastructure
Backbone: National ISP
Local/Regional ISP
Local/Regional
ISP
Residential Access
  Modem
  DSL
  Cable modem
Access to ISP, Backbone transmission
  T1/T3, OC-3, OC-12
  ATM, SONET, WDM
Internet Service Providers
  Point of Presence (POP)
Campus network access
  Ethernet
  FDDI
  Wireless

## Slide 146: Growth of the Internet in Terms of Number of Hosts
146
Number of Hosts on the Internet:
Aug. 1981 213
Oct. 1984 1,024
Dec. 1987 28,174
Oct. 1990 313,000
Jul. 1993 1,776,000
Jul. 1996 19,540,000
Jul. 1999 56,218,000
Jul. 2004 285,139,000
Jul. 2005 353,284,000
Jul. 2007 489,774,000
Jul. 2008 570,937,000
Jan. 2009 625,226,000
CAIDA router
level view

## Slide 147: The Design Philosophy of the DARPA Internet

## Slide 148: Goals
Survivability in the face of failure
Support multiple types of service
Accommodate a variety of networks
Permit distributed management of resources
Be cost effective
Permit host attachment with a low level of effort
Be accountable
. Connect different networks

## Slide 149
Survivability in the Face of Failure
Continue to operate even in the presence of network failures (e.g., link and router failures)
  as long as the network is not partitioned, two endpoints should be able to communicate…moreover, any other failure (excepting network partition) should be transparent to endpoints
Decision: maintain state only at end-points (fate-sharing)
  eliminate the problem of handling state inconsistency and performing state restoration when router fails
Internet: stateless network architecture

## Slide 150: Support Multiple Types of Service
Add UDP to TCP to better support other types of applications
  e.g., “real-time” applications
This was arguably the main reason for separating TCP and IP
Provide datagram abstraction: lower common denominator on which other services can be built: everything over IP
  service differentiation was considered (remember ToS?), but this has never happened on the large scale (Why?)

## Slide 151: Support a Variety of Networks
Very successful
  because the minimalist service; it requires from underlying network only to deliver a packet with a “reasonable” probability of success
…does not require:
  reliability
  in-order delivery
IP over everything
  Then: ARPANET, X.25, DARPA satellite network..
  Now: ATM, SONET, WDM…

## Slide 152: Other Goals
Permit distributed management of resources
Be cost effective
Permit host attachment with a low level of effort
Be accountable

## Slide 153: 计算机网络的定义
1. 计算机网络是以实现远程通信为目的，一些互连的，独
立自治的计算机的集合。
2．计算机网络是把地理位置上分散的为能够相互共享资源
（硬，软件，信息）的方式而连接起来，并且各自具有独
立功能的计算机系统之集合。
● 计算机间通信的目的是为共享硬、软件、信息资源；
● 各计算机功能独立，地域可以分散；
● 计算机网络应具有网络操作系统。
3. 计算机网络是一组相互连在一起的计算机系统的集合。
4. 凡将具有独立功能的两个以上计算机系统，通过通信设
备和线路（或无线）将其连接起来，由功能完善的网络
软件（网络协议，操作系统等）实现网络资源共享和信
息交换的系统，称之为计算机网络。

## Slide 154
Cerf and Kahn’s internetworking principles:
  minimalism, autonomy - no internal changes required to interconnect networks
  best effort service model
  stateless routers
  decentralized control
define today’s Internet architecture

## Slide 155: Summary
Covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
performance: loss, delay
layering and service models
backbones, NAPs, ISPs
history
ATM network
You now hopefully have:
context, overview, “feel” of networking
more depth, detail later in course

## Slide 156: Homework
P38: 1-03
P39: 1-10,1-11,1-17,1-19,1-20
P39: 1-22，24